## Slide 1
Ryan Beckett
with
Aarti Gupta, Ratul Mahajan, David Walker
A General Approach to Network
Configuration Verification

## Slide 2
Misconfigurations are common
Notes: Why is network verification important? Because despite best practice and decades of experience.

## Slide 3
Misconfigurations are expensive
$
$
Notes: In addition to being common, configurations are also expensive. Numerous studies that have looked at the problem have concluded that network outages caused by misconfiguration cost hundreds of thousands of dollars for every hour of downtime.

## Slide 4
Why control-plane configuration is hard
-BGP, OSPF, RIP
-Route redistribution
-Metric conversions
-Protocol parameters
-Interface metrics
-Interface filters
Complex
Low-level
Complexity
Distributed
Failures
-Device configurations
-100,000s of lines
-Link failures common
-Router failures possible
Failures
Distributed
Low-level
Bugs
Notes: One of the main reasons misconfigurations occur with such frequency is because…

## Slide 5
Many data planes
???
???
???
???
???
In the presence of certain
eBGP routes from peers
After particular
links have failed
When forwarding
a specific packet
Routes are exchanged in
a specific order
1
2
Notes: Furthermore, a single set of control plane configurations can result in a huge number of different data planes depending on the exact scenario, and some bugs will only appear in specific data planes.
Want to be proactively verify correctness under for all possible data planes that might emerge from the control plane.

## Slide 6
Progress in Network Verification
Network Design Coverage
Data Plane Coverage
Data Plane Analysis
Control Plane Analysis
HSA [1]
Veriflow [2]
Ping
Traceroute
Batfish [3]
ARC [5]
ERA [4]
Bagpipe [6]
Single
Packet
Single
Data Plane
Controllable
Data Plane
Multiple
Data Planes
All
Data Planes
[1] Kazemian et al, NSDI’12
[6] Weitz et al, OOPSLA’16
[5] Gember-Jacobson et al, SIGCOMM’16
[4] Fayaz et al, OSDI’16
[3] Fogel et al, NSDI’15
[2] Khurshid et al, NSDI’13
Notes: Fortunately, as a community, we have made some progress towards this, but we haven’t gone all the way. Here is the progress we have made so far.
Elaborate on why they don’t work (e.g., Bagpipe only works for a specific kind of BGP setup. can’t model iBGP, local-pref, etc).

## Slide 7
Is it possible to build a verification tool that achieves both high network design coverage and data plane coverage while remaining scalable enough to enable verification of many real networks?
‘‘
’’

## Slide 8
Progress in Network Verification
Network Design Coverage
Data Plane Coverage
Data Plane Analysis
Control Plane Analysis
HSA [1]
Veriflow [2]
Ping
Traceroute
Batfish [3]
ARC [5]
ERA [4]
Bagpipe [6]
Minesweeper
Single
Packet
Single
Data Plane
Controllable
Data Plane
Multiple
Data Planes
All
Data Planes
[1] Kazemian et al, NSDI’12
This Talk
[6] Weitz et al, OOPSLA’16
[5] Gember-Jacobson et al, SIGCOMM’16
[4] Fayaz et al, OSDI’16
[3] Fogel et al, NSDI’15
[2] Khurshid et al, NSDI’13

## Slide 9
Our Approach
Represent the network as a combinational circuit
Use static analysis to optimize the circuit encoding
Relates the inputs and outputs of devices with SMT constraints
Remove protocol details when possible
Any solution to these constraints represents a stable data plane
Leads to an average 460x speedup

## Slide 10
The Architecture

## Slide 11
Workflow
Vendor-Independent Format
1.
192.0.0.0 ≤ out.prefix
out.prefix ≤ 192.1.0.0
best.valid ⇒ out.lp = 120
best.valid ⇒ out.ad = 20
2.
Cisco
Arista
Juniper
Vendor-Specific Configs
3.
Circuit Encoding
Parse
Encode
4.
Output
Solve
+ Property
Interfaces: {
Ethernet0/0: {
InterfaceCost: 1,
importPolicy: “PEER_IN”,
…
}
}
Notes: Idea: (4) useful counter-example OR verified property

## Slide 12
Demo
Notes: “Minesweeper can detect violations of properties. Provide counter examples. Validate that we have fixed all the problems.”

## Slide 13
Demo: Topology
Can the border routers
always reach host1?
‘‘
’’

## Slide 14
Notes: This system will pinpoint “community, prefix length, etc that trigger the bug”

## Slide 15
Example Encoding

## Slide 16
Encoding Overview
R1
S1
S3
S2
N1
N2
N3
R2
R3
Does P hold in the network?
‘‘
’’
Network Encoding: N
Network Property: ¬ P
⋀
Satisfiable: Property Violation
Unsatisfiable: Holds for all data planes

## Slide 17
Data plane packet
1
Running Example
}
dstIp
Symbolic Packet
srcIp
dstPort
srcPort
protocol
{
R1
S1
S3
S2
N1
N2
N3
R2
R3
???
???
How does each router
forward a packet?
‘‘
’’
0 ≤
0 ≤
0 ≤
0 ≤
0 ≤
≤ 232
≤ 232
≤ 216
≤ 216
≤ 28
Notes: At the end of the day, we care about how a packet is forwarded through the network.

## Slide 18
Running Example
R1
S1
S3
S2
N1
N2
N3
R2
R3
S1
S3
S2
N1
N2
N3
OSPF
CON
BGP
BGP
OSPF
CON
OSPF
CON
R1
R2
R3
Protocol
View
Protocol Interactions
2

## Slide 19
Running Example
S1
S3
S2
N1
N2
N3
OSPF
CON
BGP
BGP
OSPF
CON
OSPF
CON
R1
R2
R3
Circuit
View for R1
Protocol Interactions
2
R1BGP
R1CON
R1OSPF
R2BGP
N1BGP
e4
in4
After R2
export filter
After R1
import filter
Redistribution
From CON to BGP
BGP peering
Between R1 and R2
Notes: Can a “routing record“ reach this point in a stable solution Define term. Black dots are routing records.

## Slide 20
Running Example
R1BGP
R1CON
R1OSPF
N1BGP
med:
}
prefix:
Routing Record
prefixLen:
adminDist:
localPref:
[0,232)
[0,28)
[0,25)
[0,232)
metric:
[0,232)
[0,232)
ospfType
[0,22)
{
valid:
1 bit
Control Plane Info
3

## Slide 21
Import FIlters
4
Running Example
R1BGP
R1CON
R1OSPF
R2BGP
N1BGP
e4
in4
ip prefix_list L deny 192.168.0.0/16 le 32
ip prefix_list L allow
route-map R1_Import_From_R2 10
match ip address prefix-list L
set local-preference 120
R1 BGP import filter from R2
if e4.valid ∧ failedR1,R2 = 0 then if ¬ (FBM(e4.prefix, 192.168.0.0, 16) ∧
16 ≤ e4.prefixLen ≤ 32) then
    in4.valid = true in4.lp = 120 in4.prefix = e4 .prefix
    in4.metric = e4.metric
    in4.prefixLen = e4 .prefixLen
    …
else in4.valid = false
else in4 .valid = false
If R2 exports a route
If it passes the import filter
Then R1 has the same
route with local-pref 120
SMT constraint
Otherwise, R1 does not
have a route from R2

## Slide 22
Decision Process
5
Running Example
R1BGP
R1CON
R1OSPF
R2BGP
N1BGP
in1
in4
in5
in7
R1-BGP-BEST = Min(in1, in4, in5, in7)
R1-OSPF-BEST
R1-BEST = Min(R1-BGP-BEST
R1-CON-BEST)
What is the best BGP route?
What is the best overall route?

## Slide 23
Decision Process
5
Running Example
R1BGP
R1CON
R1OSPF
R2BGP
N1BGP
e4
in4
RIBR1,R2 = (in4 = R1-Best)
FIBR1,R2 = RIBR1,R2 ⋀ ¬ ACL(R1,R2)
Does R1 have a RIB entry for R2?
Does R1 have a FIB entry for R2?

## Slide 24
Supported Features
OSPF Intra-area
OSPF Inter-area
eBGP Local-pref
eBGP Communities
eBGP MEDs
Implemented
Features
eBGP Aggregation
eBGP Path Prepending
iBGP
Route Reflectors
Static Routes
Route Redistribution
Multipath Routing
IPV6
Access Control Lists
Continued…

## Slide 25
Property: Reachability / Isolation
Can router R3 (not) reach subnet S2?
‘‘
’’
R1
S1
S3
S2
N1
N2
N3
R2
R3
canReachR2 ⇔ FIBR2,S2
canReachR1 ⇔
    (FIBR1,R2 ⋀ canReachR2) ⋁
    (FIBR1,R3 ⋀ canReachR3)
canReachR3 ⇔
    (FIBR3,R1 ⋀ canReachR1)
Property: canReachR3
Notes: Emphasize, reachability here is for all possible data planes

## Slide 26
Supported Properties
Reachability
Isolation
Waypointing
Path Length
2
1
0

## Slide 27
Supported Properties
Disjoint Paths
Forwarding Loops
Black Holes
Multipath Consistency
S
D

## Slide 28
Supported Properties
Load Balancing
Router Equivalence
Fault-Invariance
Network Equivalence
=
.4
.6

## Slide 29
Optimizations

## Slide 30
Optimizations: Prefix Hoisting
med:
}
prefix:
Routing Record
prefixLen:
adminDist:
localPref:
[0,232)
[0,28)
[0,25)
[0,232)
metric:
[0,232)
[0,232)
ospfType
[0,22)
{
valid:
1 bit
FBM(r.prefix, 192.4.0.0, 16) ⋀
16 ≤ r.prefixLen ≤ 32
FBM(dstIp, 192.4.0.0, 16) ⋀
16 ≤ r.prefixLen ≤ 32
=
(192.4.0.0 ≤ dstIp ≤ 192.4.0.0 + 232-16) ⋀
16 ≤ r.prefixLen ≤ 32
=
Integer Difference Logic!
Notes: Set up mental model of what costs (prefix is a bitvector for every route record) (N representations of the control plane)

## Slide 31
Optimizations: Slicing
med:
}
Symbolic Record
prefixLen:
adminDist:
localPref:
[0,232)
[0,28)
[0,25)
metric:
[0,232)
[0,232)
ospfType
[0,22)
{
valid:
1 bit
Statically analyze the configs to
determine when certain attributes
are irrelevant
Example: if the local preference
is never explicitly set, then it can
not influence the decision process

## Slide 32
Optimizations: Slicing
Maintain a single copy of export
variables when the export policy
is uniform to all peers
Merge the import and export
records when the default import
policy is used
R1BGP
R2BGP
N1BGP
e2
e3
out2
out3
R1BGP
R2BGP
N1BGP
e2
out3

## Slide 33
Evaluation

## Slide 34
Evaluation
Can Minesweeper find real bugs?
How well does Minesweeper scale?
1—23K lines of configuration
Compare verification time across a wide variety of properties
Test on a collection of synthetic data center benchmarks
Run on a collection of 152 legacy networks
Use OSPF, eBGP, iBGP, Static Routes, ACLs, Redistribution

## Slide 35
Evaluation: Bug Finding
Loopback0
Mangement interface reachability
Local equivalence of routers
Found 67 violations of the property
Found 29 violations
Example: BGP peer sends /32 with length 2
Example: ACL has missing entry
Blackholes occur only at the network edge
Reachability is the same after any 1 failure
Found 24 violations of the property
Found no violations of the property

## Slide 36
Evaluation: Scalability
Management interface reachability
Local equivalence of routers
(For all n comparisons)
< 400 ms
< 60 ms

## Slide 37
Evaluation: Scalability
Black holes only occur
at the network edge
Reachability is the same after
any single link failure
< 350 ms
< 1.5 sec

## Slide 38
Evaluation: Scalability
< 5 minutes

## Slide 39
Conclusions
Represents the network as a combinational circuit
Minesweeper is a general and scalable control plane verification tool
Our optimizations enable scaling to real networks
in1
in2
out1
out2
https://batfish.github.io/minesweeper/